## Slide 1: When subjective is not enough
Tales of Automation and searching for the objective HP measure
07 Feburary 2019 – Norrköping, Sweden
Dr. Nathan Vink – Human Performance Lead, Austro Control

## Slide 2
What is this?? What does it have to do with our brains??

## Slide 3: Scope and Contents
1. Purpose of Presentation – Problem statement
2. What do ANSPs need in the coming years. The need to move carefully through Automation scales
3. Human Performance Strategy at Austro Control
4. Objective Human Performance measures
SESAR research
Human-Machine information data is the key

## Slide 4: Background – Who am I?
Cognitive Psychology, Music History and Philosophy
PhD, MA, BA – University of Auckland, NZ
MSc in Organisational Psychology
Maastricht University
Pirate Hunter
Antarctic Explorer
Pilot
Warfare Officer, Navigator and Commanding Officer
Royal New Zealand Navy
Associate Professor
Maastricht University
Senior Human Factors Specialist at NATS
Human Performance Lead – Austro Control
Main topics: Leadership and Team Work in Safety systems, Human Performance, and Human Machine Interface Design

## Slide 5: Where is home for you?
Reminder – NZ is here!!
Born in Matamata (Hobbiton) to Dutch parents
Evicted for being too freakishly tall!
Now live in the United Kingdom

## Slide 6: The problem statement
Even the most conservative figures have demand increasing. Delay is already in the system. Human Performance effects this greatly.
Growth of traffic currently outstrips supply of competent personnel to do the job. We are losing more people to retirement than we train to replace them and meet growth

## Slide 7: The Balance...
According to a Mckinsey briefing in 2018, the Aerospace industry could see a 50 billion euro benefit from introducing more AI. Automation is included in this. More than 50% of activities (not jobs) could be automated.
Our workforce is changing dramatically. Other than pay, more employees demand flexibility above all else. Workforces change faster and demand more meaning
This demands a framework and understanding of automation on cognition
It demands an understanding of laying infrastructure and policy to meet the changing workforce

## Slide 8: As capacity is pushed higher..
Safety and Human Performance are pushed to limits
Safety Decreases (not always linear – for illustrative purposes)
Human Performance surges to deliver full capacity but does not last long

## Slide 9: Luckily, we know more and more about why
Human Performance has been long established as a key variable. Modern science continues to reveal more and more about why and how... Meaning we can take steps to improve..

## Slide 10: LoAT Model – Automation Framework
The Levels of Automation Taxonomy is a four tier structure looking at:
    Information Acquisition
    Information Analysis
    Decision Making
    Action Implementation
It has been used successfully in a number of current SESAR projects as well as other areas of internal research
The model has demonstrated usefulness not only for framing discussions and identifying issues, but because quantifiable results can be captured from data in systems.
It has highlighted the Human Cognition elements as well
It can be used to look at ‘high-level’ operations in general but also is versatile to be used for individual technology and airspace projects

## Slide 11
Decision Making and Planning
Action Execution
Working / Short Term Memory
Situation Awareness
Attention and Perception
Long Term Memory
Adapted from Wickens, C.D., Engineering Psychology and Human Performance, Harper Collins, New York, 1992.
The automation areas make sense in terms of Cognition
Notes: MN / ML
Go through the answers

## Slide 15: SESAR Human Performance (HP) Background
PJ10.02b: Advanced Separation Management: NATS addressed Systemised Airspace in the lower airspace and the need for automatic Non-Conformance and Resolution tools
PJ16.04: CWP HMI and in particular Multi-Touch and Speech Recognition support
Both areas have looked at levels of Automation in current environments and future states.
Recognition of a current ‘stasis’ and ‘end goal’ but warning over the transition to end goals, particularly for the human operators

## Slide 16: PJ.10-02b Overview
- PJ10.02b investigates further steps towards a higher level of automation in separation management. It consists of advanced tools support for controllers, enabling increases in safety and capacity. The tools support the controller in monitoring tasks, show conflicting or dependent aircraft, proposing and selecting conflict free clearances.
- PJ10.02b has six different threads and environments. The NATS case focuses on systemised airspace proposals for the London TMA. This would see multiple simultaneous PBN routes bringing aircraft in and out to set points within the TMA.
LoAT was first used to map the current Operational (high-level view) with reference to tool support in general.
It was then used to look at what elements (levels) of separation management automated tools would be needed to deploy the solution. Controllers estimated that they would need to make a large leap from C2 to C5 and from D2 to D6 or above. This is a significant finding as it shows a key threshold that needs to be further researched. In this sense, the LoAT has been extremely useful at pointing out priorities for further research

## Slide 17: PJ10.02b Case Study
A Standard SID out of Gatwick has 3-4 level offs.
This is due to Heathrow out bounds and Luton/Stanstead inbounds
Every level bust is crucial because of this.
Systemised airspace could see multiple simultaneous non-conformances
Controllers currently make a reaction in split seconds
Providing steps of automation may be too cumbersome
Thus, it will be ‘all or nothing’ and assurance will need to be greater than the current amount of Human Error

## Slide 18: Moving through the levels
Chart: Current Automation Levels by Operation
| Action Implementation | Decision and Action Selection | Information Analysis | Information Acquistion
TMA | 1 | 1 | 1 | 2
En-Route | 1 | 2 | 5 | 4.5
Airports | 1 | 1 | 2 | 1.5
PJ10.01b – Modelling the Eurocontrol Automation Levels

## Slide 19: What does Automation have to do with it?

## Slide 20: CANSO Standards of Excellence
Introduced in 2019, Austro Control took part as one of Six ANSPs to Test the model across the operations.
The SOE is now an international baseline and measurement tool for assessing HP Management and success

## Slide 21: SoE in HPM - results & proposed target levels
Study Area | Element | Level 2019
1. | Policy, Strategy, Resources | B
2. | Health and Wellbeing | C
3. | ATM Equipment and Support Tools | C
4. | Operational Procedures | D
5. | Teamwork and Communication | C
6. | Operational Training | D
7. | Selection | D
8. | Impact of Change | B
9. | Leadership | A
10. | Roles and Responsibilities | B
11. | Human Performance Investigation and Learning | C
12. | Human Performance Management Assurance | A
2019 (12) | Level E | 0
 | Level D | 3
 | Level C | 4
 | Level B | 3
 | Level A | 2
Target level 2020
B
C
C
D
C
D
D
B
B
B
C
B
Target level 2021
C
D
D
D
D
D
D
C
C
C
D
C
CANSO Standards of Excellence

## Slide 22: Our HF strategy aims to integrate

## Slide 23: Human Performance Strategy 2020 - 2030
Please contact Nathan directly to learn more – The Austro Control strategyy is not yet fully published and so not released here.

## Slide 24: A short break
Summary so far:
Any research into human performance must be conscious of what it will take to shift an ANSP’s position. The Automation framework allows us to identify the correct element to tackle
A new tool or solution must be Safe and allow us to move between the levels safely without compromising efficiency and workload

## Slide 26: What can Netflix teach us about HP?
Founded in 1997 as a Video order service
As late as 2007 this was the model then something changed
Began a streaming service 2008
Entered content production in 2012
By 2016 Netflix operates in 190 countries
2013 First Emmy award for House of Cards
By 2018 most nominated production company
2018 First Oscar
How did they do it??

## Slide 27: Types of HP Measures
Cost is not just investment in technologies, it is also the human effort required to collect and process
Usefulness of course is variable and the right conditions must always be set for criterion validity

## Slide 28: Types of HP Measures
Cost is not just investment in technologies, it is also the human effort required to collect and process
Usefulness of course is variable and the right conditions must always be set for criterion validity

## Slide 29: For Reference – Existing HP Measures
 | WL | Stress | Fatigue | SA | Attention | Vigilance | Trust | Motivation | Viability Notes
Objective Measures |  |  |  |  |  |  |  |  | 
Echo Cardiogram (ACG) | X | X | X | X | X | X |  |  | 
EEG | X |  | X | X | X | X |  |  | Intrusive, much effort
EMG | X | X | X |  |  |  |  |  | 
EOG | X | X | X | X | X | X |  |  | 
fNRI | X |  |  | X | X |  |  |  | The collection of Health related data has been excluded by the project due to ethics permissions.
GSR/EDA | X | X | X |  |  |  |  |  | 
Respiratory | X | X | X |  |  |  |  |  | 
Eye Tracking | X | X | X | X | X |  |  |  | May have medium accuracy
Ergonomic Measures (ISO Standards – e.g. Rapid Upper Limb Assessment) |  | X | X |  |  |  |  |  | 
Seat Sensors | X | X |  |  |  |  |  |  | 
Voice Analysis | X | X |  | X |  |  |  |  | 
Mouse Clicks / Tracking | X |  |  | X | X | X |  |  | Easy to log
Keyboard Strokes | X |  |  | X | X |  |  |  | Easy to log
Reaction Times | X | X | X | X | X | X | X |  | Start and end time of reaction sometimes hard to identify (thinking)
Subjective: |  |  |  |  |  |  |  |  | 
User Acceptance (perceived acceptability) | X | X | X | X | X | X | X | X | 
Bedford Workload Index | X | X |  |  |  |  |  |  | 
NASA Task Load Index | X |  |  |  |  |  |  |  | Often Used, therefore good comparability
China Lakes SA Measure |  |  |  | X |  |  |  |  | 
Picture Scale Measures |  |  |  | X |  |  |  |  | 
Instantaneous Self-Assessment | X | X | X | X | X | X | X | X | Quick and Easy Method
Eurocontrol SHAPE questionnaires (e.g. SASHA and SATI) (11 and 12) | X |  |  | X |  |  | X |  | 
Expert Observations (over the shoulder) | X | X | X | X | X |  |  | X | 
Situational Awareness Rating Technique |  |  |  | X | X |  |  |  | 
Situational Awareness Global Assessment Technique (SAGAT) |  |  |  | X | X |  |  |  | Intrusive

## Slide 30: The Ontology

## Slide 31: The Algorithm
Raw Data (from Systems)
Static Data (from other systems)
UPMS Component: a side story
Pre-processing: the hardest part!
The Neural Network: looking for correlations
The Ontology: Identifying what it all means
The TA (subjective at first): deciding what busy is
Visualisation: Giving it to those who need it
Machine Learning: learning from outcomes

## Slide 32: In More Details

## Slide 33: How it Works

## Slide 34: An Example of all the types of tasks
Taken from Vienna and Prague Approach Ontology – PJ16.04

## Slide 35: Of course its not just about machine interactions...
The examples show how the basis of the Ontology began with ‘known’ human-machine interractions
But... A lot of cognitions are not represented by machine interactions...
This is where you have two options:
  Interviews and task analysis reveal the ‘thinking’ workload as subjectively measured
    E.g. What to do in a non-conformance
  The black-hole Halo: i.e. Using Machine Learning to infer the cognition time
    This will be the next step in development
    We already have data on this

## Slide 36
For Boxes (20 nm x 20 nm x 3000 ft x 1h):
For sectors:
Combined with weather:
Link to Complexity and MET
Austro Control has projects for Complexity and MET. When HP is overlayed, the power for Supervisors and Operational decision making is further enhanced...

## Slide 37: Results – Sector specific capacity tables

## Slide 38: Real time workload for Supervisors
Real time workload per minute (or finer if necessary)
Improved decision making by GS and OS
Best practice MOPs identification
Validation of technology projects for usability, acceptability, WL and SA

## Slide 39
For Boxes (20 nm x 20 nm x 3000 ft x 1h):
For sectors:
Combined with weather:
Link to Complexity and MET
Austro Control has projects for Complexity and MET. When HP is overlayed, the power for Supervisors and Operational decision making is further enhanced...
For Illustrative purposes so far...

## Slide 40: Design and Assurance assistance
Priorities for Automatic Non-Conformance tools
Notes: Current objective data indicates where the most common non-conformances are occurring and thus would set the priorities for what information needs to be more automated in a systemised airspace environment

## Slide 41: Longer Term Implications and Next Steps
Computer generated job descriptions
Pinpoint human error
Better design decisions on HMI, Automation and traffic capacity
Computer generated ‘optimal airpsace’ designs based on Human Performance
Safe and Controlled implementation of new technologies and automation
Individual analysis for training, occurrences and general human performance
Outside of ANS – enhanced understanding of general cognition in Human Beings
Support for the Cumulative Prospet Theory and Systems 1 and 2 thinking of Daniel Kahneman

## Slide 42: Next Steps – Integration and Infrastructure

## Slide 43: Facilitating Research and Links
HAWAII SESAR ER4 Bid
SESAR Wave 2 PJ10 Sln 96 – Continuation of PJ16.04 on Speech recognition, eye tracking and user profiles
Digital ANS work in COOPANs)
Eurocontrol Scientific Community on Automation
CANSO Human Performance Standards
Link to Austrocontrol Heading 030, Human Performance Strategy/Campaign and Assurance enhancements

## Slide 44: Obstacles
Need to get more data! 
Strategy and infrastructure for extracting meaningful data
‘Smarter’ workstation designs
Validation and safety cases for making decisions based on this kind of data
Potential Privacy concerns – should be alleviated by ‘system’ view rather than ‘individual’ view
Industry partners to change their approach to system development – e.g. some core code changes to Topsky

## Slide 45: Danke Schön und Liebe Grüße!
Questions? Fragen? Frågor?
For more information please do get in touch:
Nathan.vink@austrocontrol.at
Linkedin: nathanvink