## Slide 1: Data Transmission and Base-Station Placement for Optimizing Network Lifetime Esther M. Arkin and Joseph S. B. Mitchell Stony Brook University Swaminathan Sankararaman, Javad Taheri Alon Efrat, Srinivasan Ramasubramanian U of Arizona Valentin Polishchuk U of Helsinki

## Slide 2: Problem Formalization (1)
Given: a set of sensors S={s1…sn}, and a basestation BS. Need to find a topology – a forwarding scheme (who sends data to whom) to prolong the time the first sensor die.
Assumptions:
Each sensor generates F bits/second, all have to reach the basestation (no bit is left behind).
All sensors have identical batteries.
Rayleigh fading model - energy needed for sending a bit xy increases as distance squared.
BS
s1
s13
s14
s34

## Slide 3: More Interesting Problem
Where should we place the Basestation to maximize system’s lifetime ?
BS
s1
s13
s14
s34

## Slide 4: Topologies – what is this obsession about trees.
(and what about interference ?)
Answer: We assume that sensors are deactivated for long periods (sleeping). In a tree topology, clock synchronization is relatively easy, comparing to arbitrary DAGs.

## Slide 5: And what’s the deal with 2-trees ?
We would consider only topologies which are trees where each sensor is of distance ≤ 2 from the basestation.
Delay time is limited
Simplicity of protocol
3-trees (or more) are NP-Hard (in this paper)
Polynomiallity.
Side comment – if any DAG solution is acceptable then a simple LP solution finds optimum forwarding scheme for the fixed BS problem (in ideal conditions)
For the dual problem where the BS location need to be found, a (1-ε) approximation algorithm exits [Efrat, Har-Peled, Mitchell 05]

## Slide 6: Fixed BS - the decision problem
Given a time duration τ either find a forwarding scheme that enables the system to survive this duration, or determine that no such topology exist.
Algorithm –
compute d* - the crucial radius – for which a sensor within this distance could transmit all its data directly to the basestation (no relaying is needed) for time τ. Observe that d* is universal to all sensors.
Find the set of cluster-heads – sensors within distance d* from BS. The other sensors are leaves.
d*
BS
Next need to find an assignment specifying which leaf to connect to which ClusterHead

## Slide 7: Computing the assignment
A ClusterHead si can transmit all its own data for time duration τ
In addition, possibly it could relay other sensors’ data – depending on its distance d(si , BS).
Let ci denote the number of other sensors si can relay.
The assignment problem: Need to connect each leaf sj to a ClusterHead si such that
d(si , sj ) ≤ d*
The number of sensors relayed by si
  cannot exceed ci
d*
BS
sj
si
Smells somehow like bipartite matching

## Slide 8: Computing the assignment-cont
Connect each leaf si to a ClusterHead si such that
d(si , sj ) ≤d*
The number of sensors connected to si ≤ ci
Def:
  This assignment is perfect if all leaves are connected.
  ClusterHead si is saturated if it is assigned to ci leaves.
  E the set of all edges between pairs (leaf, CH) whose distance is ≤ d*.
BS
sj
si
Warmup Lemma: Assume M is an assignment at which leaf sj is not assigned to a CH. Then if a perfect assignment exists then there is an augmenting (alternating) path π
  starting at sj
  ending at non-saturated ClusterHead si
  alternating between edges of E which participates (resp. does not participate) in the assignment.
Proof – immediate from flow algorithms
1
1
1

## Slide 9: Computing the assignment
To obtain efficient algorithm, we need to recycle some ancient results:
Given a set of unit disks S={D1, ..Dn} in the plane, we have a data structure that supports
- Finding a disk of S containing a query point q
- Deleting this disk
Each in O(log n) time. [Efrat, Katz, Itai 95]
Applications: Assume that
  the centers of the disks are
  the ClusterHeads,
  the radius of the disks is d*
  q is actually a leaf sj
Then by repeating these operations we can find all Clusterheads which are neighbors of sj.
q
  Actually, we can grow a BFS trees of alternating paths, rooted at sj in O(n log n) time.

## Slide 10: Computing the assignment
By expanding Dinic’ matching algorithm, we can actually find the assignment in O(n3/2 log n)
If an edge is deleted/inserted, or if ci is incremented/decremented, we can update the assignment in O( n log n) per event
Next lets find optimum location of the basestation

## Slide 11: Orbits around si for a fixed duration τ
si
si can transmit its data to any point in this disk for duration τ
si can transmit all its data, and data relayed from 1 another sensor
si can transmit all its data, and data received from 2 other sensors

## Slide 12: Finding opt location of a basestaion – fixed duration
For each sensor compute its orbits.
We compute the assignment at each vertex of this arrangement (using previous algorithm)
O(n log n) per vertex,
or O(n5 log n) altogether

## Slide 13: Finding optimum duration
Use parametric search of Megiddo + improvements by Cole
Use AKS sorting networks to sort the vertices between disks. This is the generic algorithm generating critical durations τ
Use previous algorithm as an oracle to determine if τ is too small/large

## Slide 14: Finding 3-Level Trees is NP-Hard
Hard even in the case of finite data transmission (no issue of maximizing lifetime).
Maximum distance to which sensor can transmit data of x sensors:
  dx = x−(1/ α) , for some 2 ≤ α ≤ 4
Decision Problem:
Given a set of sensors S and a location of the base-station BS, does there exist a transmission protocol (with arbitrarily many levels) enabling all sensors to transmit their data to BS.
Reduction from 3-PARTITION Problem:
Given a set of integers a1, . . . ,a3n, where each ai is between B/2 and B/4 for B = Σ ai/n = O(1), decide if it is possible to split them into n groups of 3 so that the sum of the integers in every group is the same.

## Slide 15: Construction
For an instance of 3-PARTITION, place 3 types of sensors:
  n clusterheads (c) at distance dB+1 to the left of BS
  3n elements (i) on semicircle of radius dB/2 around c away from BS (close to the horizontal line)
  ai−1 atoms (si) at distance d1 on ray from c through i where
  B/4 ≤ ai ≤ B/2
Solution for Decision Problem (if there exists a tree)
↕
Solution for 3-PARTITION (partition element sensors into groups of 3 transmitting to same clusterhead)

## Slide 16: Proof
Idea: elements i grouped according to solution of 3-PARTITION
Forward: 3-PARTITION implies 3-Level Tree
  Elements in each group transmit to one clusterhead
Backward: 3-Level tree implies 3-PARTITION
  Atoms must transmit to elements
  Elements cannot transmit directly to BS, since
  dB+1 + dB/2 > dB/4,
  Hence, elements must transmit to c
  Elements must be split evenly among clusterheads, since no clusterhead can transmit more than B+1 sensors